## Slide 1: Brief look at three real-world uncertainty propagation case studies
Pesticide leaching in soil
Streamline network derivation from a digital elevation model
Geometric correction of airborne imagery

## Slide 3: GeoPEARL has many inputs: mainly soil, landuse, climate and hydrology

## Slide 4: GeoPEARL inputs considered uncertain:
Soil properties:
Horizon thickness
Texture
Organic matter content
Hydraulic conductivity
Water retention characteristic
Pesticide properties:
Half-life of transformation in soil
Coefficient of sorption on organic matter

## Slide 5: Netherlands represented by a grid sample of 258 points
At each point 1000 Monte Carlo runs of GeoPEARL
Next the 90 percentile (P90) of 258 GeoPEARL outputs computed for each of the 1000 runs
Variability in the 1000 P90 values conveys uncertainty about true P90

## Slide 6: Uncertainty in GeoPEARL output
Large uncertainty in P90, particularly for substance D
Box-plots straddle the regulatory limit of 0.1 g∙l1
Risk-aversive policy would reject all three pesticides
D
A
B

## Slide 7: Pesticide properties are main source of uncertainty
 | Organic matter | Other soil properties | Half-life | Sorption
Substance D | 0 | 0 | 60 | 20
Substance A | 7 | 1 | 54 | 41
Substance B | 7 | 0 | 87 | 10
Percentage variance explained by uncertain inputs

## Slide 9: Monte Carlo approach as before

## Slide 10: 100 realisations of stream network and error box plots for curvature classes
concave
convex

## Slide 11
Italy
Study area

## Slide 12: Geometric correction with an elevation map (DEM)
2500
2000
1500
0
1000
500
Height (m)

## Slide 13
Uncertainty
Propagation
Analysis
Sample from PDF
N samples
Level0 product
Level 1 product
Level 2 product
Analyse
Run Model 2 N times
PDF input parameters
Run Model 1 N times
Quality layers
PAF

## Slide 14: Uncertainty Digital Elevation Model (DEM) Create a Probability Distribution Function (PDF)
Temme et al. 2009, Geostatistical Simulation and Error Propagation in Geomorphometry
Create variogram
Distance (in pixels)
Semivariance
2500
2000
1500
0
1000
500
Height (m)
10
20
30
10
20
30
40
50
60
Variogram defines how DEM error is
correlated with distance  Spatial correlation
Notes: Spatial correlation: modeled by variogram; Variogram defines how DEM error is correlated with distance

## Slide 15: Uncertainty Digital Elevation Model (DEM) Generate samples of uncertain inputs
Simulated DEM
Error (m)
Control Points
Error map
Original DEM
2500
2000
1500
0
1000
500
Height (m)
40
20
0
-20
-40

## Slide 16
Sd (m)
0
16
8
Standard deviation X-coordinates
Standard deviation Y-coordinates
Magnitude of errors in x- and y-coordinates larger in off-nadir angles and in mountainous parts of the study area

## Slide 17
Zooming in shows effect of DEM error on geometric correction

## Slide 18
Zooming in shows effect of DEM error on geometric correction