## Slide 1: spup – an R package for uncertainty propagation analysis in spatial environmental modelling
Kasia Sawicka and Gerard B.M. Heuvelink
(with contributions from Dennis Walvoort, Stefan van Dam and Damiano Luzzi)
This project has received funding from the European Union’s Seventh Framework Programme for research, technological development and demonstration under grant agreement no 607000.
Underlying methodology
Functionality
Examples
Planned applications
Acknowledgements
Oval shapes are clickable

## Slide 2: Underlying methodology
Monte Carlo approach principle
Variable 1
Variable 2
Model run (e.g.
Output = Var1 x Var2)
Sampling
Sampling
c(10, 14, 3, 16, ....)
2
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Oval shapes are clickable
Underlying methodology
Functionality
Examples
Planned applications
Notes: The principle of how it all works using Monte Carlo approach is as follow:
The user characterises uncertain model inputs with probability distribution functions (PDFs) and appropriate correlation model.
Repeatedly sample from (spatial) PDFs.
Run model with sampled inputs and store model outputs.
Compute summary statistics of the model outputs.

## Slide 3: spup functionality
Import data and objects and define UM
Visuali
zation of results
Model call and simulations
Monte Carlo sampling techniques
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Oval shapes are clickable
Underlying methodology
Functionality
Additional functionality for analysis with ‚external’ models
Imports: gstat, magrittr, mvtnorm, purrr, raster, whisker
Available on CRAN and GitHub
Examples
Planned applications
Notes: Functions that allow user to define uncertainty model (UM):
Functions that quantify uncertainty propagation by sampling from uncertain inputs and running the model with sampled realizations:
Functions that allow user to save output in a format of data or images:
Model as:
As a function in R
Outside R call
Model used externally

## Slide 4: Defining uncertainty model (UM)
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Oval shapes are clickable
Underlying methodology
Functionality
More details
Examples
Planned applications
Notes: For uncertain spatially distributed continuous variables, such as elevation, rainfall or soil organic carbon content, we assume the following geostatistical model:
is the (deterministic) mean of the variable of interest , is a spatially variable standard deviation associated with the prediction
is simulated as a map a standardized, zero-mean, spatially auto-correlated residual modelled a correlogram.
– and this is actually sampled using stochastic spatial simulation.
Application of the Monte Carlo method to uncertainty propagation with operations that involve spatial interactions requires the simultaneous generation of realisations from the spatially distributed inputs, implying that spatial correlation should be accounted for.
For uncertain spatially distributed continuous variables, such as elevation, rainfall or soil organic carbon content, we assume the following geostatistical model:𝑍(𝑥)= 𝜇(𝑥)+ 𝜎(𝑥)∙𝜀(𝑥)
𝜇 is the (deterministic) mean of the variable of interest 𝑍, 𝜎 is a spatially variable standard deviation associated with the prediction 𝜇
𝜀 is simulated as a map a standardized, zero-mean, spatially auto-correlated residual modelled a correlogram.
– and this is actually sampled using stochastic spatial simulation.

## Slide 5: Defining uncertainty model (UM)
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Oval shapes are clickable
Underlying methodology
Functionality
Examples
Planned applications
Notes: For uncertain spatially distributed continuous variables, such as elevation, rainfall or soil organic carbon content, we assume the following geostatistical model:
is the (deterministic) mean of the variable of interest , is a spatially variable standard deviation associated with the prediction
is simulated as a map a standardized, zero-mean, spatially auto-correlated residual modelled a correlogram.
– and this is actually sampled using stochastic spatial simulation.
Application of the Monte Carlo method to uncertainty propagation with operations that involve spatial interactions requires the simultaneous generation of realisations from the spatially distributed inputs, implying that spatial correlation should be accounted for.
For uncertain spatially distributed continuous variables, such as elevation, rainfall or soil organic carbon content, we assume the following geostatistical model:𝑍(𝑥)= 𝜇(𝑥)+ 𝜎(𝑥)∙𝜀(𝑥)
𝜇 is the (deterministic) mean of the variable of interest 𝑍, 𝜎 is a spatially variable standard deviation associated with the prediction 𝜇
𝜀 is simulated as a map a standardized, zero-mean, spatially auto-correlated residual modelled a correlogram.
– and this is actually sampled using stochastic spatial simulation.

## Slide 6: Monte Carlo sampling
Oval shapes are clickable
Underlying methodology
Functionality
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
S3 methods for MC sampling from uncertain inputs
More details
Examples
Planned applications

## Slide 7: Monte Carlo sampling
Oval shapes are clickable
Underlying methodology
Functionality
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
S3 methods for MC sampling from uncertain inputs
More details
Examples
Planned applications

## Slide 8: Propagation through the model
Oval shapes are clickable
Underlying methodology
Functionality
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Run any model written as R function with a MC sample of uncertain input and additional parameters/inputs
More details
Examples
Planned applications
Notes: The output of the propagation is post-processed. The you can use it in the vusializations functions.

## Slide 9: Propagation through the model
Oval shapes are clickable
Underlying methodology
Functionality
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Run any model written as R function with a MC sample of uncertain input and additional parameters/inputs
More details
Examples
Planned applications
Notes: The output of the propagation is post-processed. The you can use it in the vusializations functions.

## Slide 10: Visualization of the results
Oval shapes are clickable
Underlying methodology
Functionality
D
Define UM
R
Realiza-tions
P
Propag-ation
R
Realiza-tions
V
Visualizations
Spatial correlogram
Adjacent maps
Correlations
R is a powerful visualization tool so can make a use of existing functionality
Glyphs
Histograms
Categorical data
Examples
Planned applications
Notes: Adjacent maps: Two maps were placed next to each other, displaying the predicted value map on the left and the uncertainty on the right for continuous data. For categorical data, the left map displayed the most likely class and the right map the associated class probability.
The second static method - Glyphs can encode data through various variables such as size, shape and colour (only used for continues data)

## Slide 11: Examples
Oval shapes are clickable
Underlying methodology
Functionality
Example 1
Example 2
Examples
Planned applications
Uncertainty propagation analysis with cross-correlated numerical variables – predicting soil C/N ratio from soil organic carbon and total nitrogen content
Uncertainty propagation analysis with a model writen in C – simple linear regression model with uncertain scalar parameters
1
2

## Slide 12: Examples (1) – uncertainty propagation with cross-correlated vars.
Oval shapes are clickable
Underlying methodology
Functionality
Examples
Planned applications
Predicting soil C/N ratio from soil organic carbon and total nitrogen content in south region of lake Alaotra in Madagascar
1.
2.
4.
3.
Data source:ISRIC Soil Grid database (www.soilgrids.org) (Hengl et al., 2017)
)
- repeat the same for TN
100
Identify areas that are suitable for crop production with 90% certainty
1
2

## Slide 13: Examples (2) – uncertainty propagation with ‚external’ models
Oval shapes are clickable
Underlying methodology
Functionality
1
2
Examples
Planned applications
Simple linear regression model written in C with uncertain scalar parameters
Spatial (or other) inputs to the models are often stored in ASCII files. In that case, when using external models in R we need code to:
Modify ASCII input file.
Run the external model.
2
1
Modifying ASCII files - rendering

## Slide 14: Examples (2) – uncertainty propagation with ‚external’ models
Oval shapes are clickable
Underlying methodology
Functionality
1
2
Examples
Planned applications
Simple linear regression model written in C with uncertain scalar parameters
Spatial (or other) inputs to the models are often stored in ASCII files. In that case, when using external models in R we need code to:
Modify ASCII input file.
Run the external model.
2
1
Running external models
To perform the uncertainty propagation analysis we need to derive multiple realizations of the model output in steps as follows:
1. Render the template, 2. Run the model,
3. Read the results. 4. Process the results.
For example:

## Slide 15: Planned applications
Uncertainty propagation analysis with process-based model LandscapeDNDC
Uncertainty propagation analysis with Metaldehyde Prediction Model
Haas et. al. (2013)
River
High risk areas
Auto-sampler locations
Risk map
Radar rainfall data
Oval shapes are clickable
Underlying methodology
Functionality
Examples
Planned applications
Notes: The planned application of ‘spup’ currently includes: uncertainty propagation analysis with LandscapeDNDC - a very complex process-based model for simulation of biosphere-atmosphere-hydrosphere exchange processes.
Another study case for ‘spup’ application will be with Metaldehyde prediction model which basing on risk area maps developed from rainfall data calculates the time of closing the abstraction points if necessarry. As the metaldehyde is a pollutant that cannot be treated the water supplier needs to know when to control the water source abstraction points.

## Slide 16: Acknowledments
Damiano Luzzi
Stefan van Dam
Sytze de Bruin
Dennis Walvoort
QUICS fellows and partners
EU funding
https://github.com/
ksawicka
‘spup’ repository
Oval shapes are clickable
Underlying methodology
Functionality
Examples
Planned applications